## Slide 1: Current-Sensing Efficient Adder for Processing-in-Memory Design
Joonseop Sim, Mohsen Imani, Woojin Choi, Yeseong Kim and Tajana Simunic Rosing

## Slide 2: Conventional
Processor
Memory
Channel
Memory is just a storage device
Write
Read
Operation throughputs are limited by memory bandwidth
Big data processing requires more computations to memory

## Slide 3: PIM approach
Processor
Memory
Channel
Write
Read
PIM
Relax the bandwidth bottleneck
Put processing units inside memory

## Slide 4
Prior Research on NVM-PIM
Sum
Cout
Bitwise(NOR, IMP)-based ADD/MUL : e.g. MAGIC[3], Stateful logic[4]
  Arithmetic functions with many cycles and intermediate states
Bitwise Operations limited : e.g. Pinatubo[1], MPIM[2]
  Not support arithmetic operations
  Cause much higher latency and extra cells consumption
[6] MAGIC, Mohsen Imani, et al, DAC 2017
[3] IMP, S. Kvatinsky, et al, VLSI, 2014
12 cycles + 11 intermediate states
136 cycles + 134 intermediate states

## Slide 5
This Work
Prior Work
(Bitwise ADD)
This Work (LUPIS)
Input
Intermediate
Intermediate
Intermediate
Output
Input
Output
Many cycles
Many
intermediate states
Latency delay
Area penalty
Single cycle ADD
Fast & no additional cell

## Slide 6
Design Overview
Bank
MAT
Row Decorder
Chip
Bank
Global Selector
Bank I/O
Local Selector
MAT
Modified
Sensing Circuit
Modified S/A
W/B
Key contributions
  Thyristor optimization (D)
  Sensing circuits modification (C)
  Efficient carry save addition (A)

## Slide 7
Thyristor Latch-Up
I
P
N
P
N
Gate
A
B
P
N
P
G
A
N
P
N
B
PNP
NPN
G
A
B
Ishort
Thyristor
  PNPN structure
  equivalent to two cross-coupled bipolar junction transistors (BJTs)
  When one of the two BJTs gets forward biased, it feeds the base of the other BJT
  Latch-up occurs at VLU and the current through the cell (i.e., from A to B) abruptly increases
Design goal : To enable Sum (XOR) function in resistance sensing circuit

## Slide 8
Modified Sensing Circuit
A | B | CIN | IBL
0 | 0 | 0 | I000
0 | 0 | 1 | I100
0 | 1 | 0 | 
1 | 0 | 0 | 
0 | 1 | 1 | I110
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | I111
Local Selector
When three rows are activated
IBL are grouped into I000, I100, I110, I111 according to Rlow(1) and Rhigh(0) combinations.

## Slide 9
A | B | CIN | IBL | COUT | Sum
0 | 0 | 0 | I000 | 0 | 0
0 | 0 | 1 | I100 | 0 | 1
0 | 1 | 0 |  | 0 | 1
1 | 0 | 0 |  | 0 | 1
0 | 1 | 1 | I110 | 1 | 0
1 | 0 | 1 |  | 1 | 0
1 | 1 | 0 |  | 1 | 0
1 | 1 | 1 | I111 | 1 | 1
GND
I000
V
I
VTHR
VDD
)
I100
I110
I111
Modified Sensing Circuit
Cout :
  IBL is copied to I1
  V1 follow dotted line as IBL  MAJ behavior
Sum :
  IBL is copied to I2
  0 at I000 since V2 < VTHR
  1,0 at I100,I110 since V3 follow blue line
  1 at I111 since V3 drop due to thyristor latch-up
VLU
Cout
Sum
0
0
1
1
0
1
0
1
Notes: V1, V2 font enlarge

## Slide 10
Make N additions independent with no carry propagation
Propagate carry only in the last stage
3 inputs to 2 outputs (3:2) reduction
Carry Save Addition : APIM[6]
Drawback : Interconnect requires large number of transistors
   Significant area overhead
Interconnect
Interconnect
Interconnect

## Slide 11
LUPIS generates ADD results at the sensing circuits and writes them back to the memory directly.
Carry Save Addition : APIM[6]  LUPIS
LUPIS does not require the expensive interconnects
Interconnect
Interconnect
Interconnect
X
X
X

## Slide 12
Experimental Setup
Device simulation : Sivaco ATLAS TCAD
Circuit-level simulations : Cadence Virtuoso and Spectre simulators with 45nm CMOS Technologies
VTEAM memristor model [5] for our memory design simulation:
  RON and ROFF of 10kΩ and 10MΩ respectively
Four OpenCL applications:
  Sobel, Robert, Fast Fourier transform (FFT), DwHaar1D
Compared with state-of-the-art GPU (AMD Southern Island, Radeon HD 7970 device) and PIM Accelerator (APIM [6])

## Slide 13
Device Simulation (by Silvaco)
Design a lateral PNPN structure
Process condition was optimized to get the conditions of a VLU of 0.98 V, a RH of 1.9 MΩ, and a RL of 1.7 KΩ
Achieved process window by tuning the ND/NA and d1/d2

## Slide 14
Energy and Performance
 | [4] | [3] | [6] | [7] | This Work
No. Memristors | 3N+5 | 3N+3 | 3N+8 | N+2 | 3N
No. Cycles | 136 | 29 | 13 | 9 | 1
Cell efficiency | 38% | 50% | 27% | 33% | 100%
Latency | 149.6ns | 31.9ns | 14.3ns | 9.9ns | 33.3ps
Energy | 3237fJ | 690fJ | 289fJ | 214fJ | 7.9fJ
Performance of 1-bit Adder for LUPIS and other technologies
Proposed LUPIS achieved superior cell efficiency, speedup and lower energy consumption due to a single cycle ADD with no extra cell penalty.
As compared to the state-of-the PIM accelerator [6], the results present 12.7X and 20.9X higher efficiency for speedup and energy respectively .
Notes: Put just 2 line, text

## Slide 15
Chart: 
| APIM [6] | LUPIS
No. cycles | 13 | 2
Overhead
LUPIS has 21% area overhead, 15x better than the APIM [6] since no additional cells are required and it took insignificant modifications to the conventional CSA circuit.
Latency overhead is just one cycle caused by the write back inclusion
Overhead
Chart: 
| APIM [6] | LUPIS
Area overhead (%) | 333 | 21
2
Notes: Text
Yeseong

## Slide 16
Conclusion
We presented a high performance PIM technology by enabling single-cycle ADD and improving the MUL performance.
Our design addresses the low cell-efficiency of other PIM technologies by executing the calculations in the sensing circuitry.
Proposed design can achieve 12.7X speed up, 20.9X lower power consumption compared to a state-of-the-art PIM accelerator.

## Slide 17
Reference
[1] S. Li, C. Xu, Q. Zou, J. Zhao, Y. Lu, and Y. Xie, “Pinatubo: A processing-in-memory architecture for bulk bitwise operations in emerging non-volatile memories,” in Design Automation Conference (DAC), 2016
[2] M. Imani, Y. Kim, and T. Rosing, “Mpim: Multi-purpose in-memory processing using configurable resistive memory,” in Design Automation Conference (ASP-DAC), 2017 22nd Asia and South Pacific, pp. 757–763, IEEE, 2017
[3] S. Kvatinsky, G. Satat, N. Wald, E. G. Friedman, A. Kolodny, and U. C. Weiser, “Memristor-based material implication (imply) logic: Design principles and methodologies,” IEEE Transactions on Very Large Scale Integration (VLSI), 2014
[4] E. Lehtonen and M. Laiho, “Stateful implication logic with memristors,” in Proceedings of the 2009 IEEE/ACM International Symposium on Nanoscale Architectures, pp. 33–36, IEEE Computer Society, 2009.
[5] S. Kvatinsky et al., “Vteam: a general model for voltage-controlled memristors,” TCAS II, vol. 62, no. 8, pp. 786–790, 2015.
[6] M. Imani, S. Gupta, and T. Rosing, “Ultra-efficient processing inmemory for data intensive applications,” in Proceedings of the 54th Annual Design Automation Conference 2017, p. 6, ACM, 2017
[7] A. Siemon, S. Menzel, R. Waser, and E. Linn, “A complementary resistive switch-based crossbar array adder,” IEEE journal on emerging and selected topics in circuits and systems, vol. 5, no. 1, pp. 64–74, 2015.

## Slide 18
Backup slides

## Slide 19
Chart: 
| TC-Adder | LUPIS
No. cycles | 9 | 2
Overhead
LUPIS has 21% area overhead, 10x better than the TC-Adder [7] since no additional cells are required and it takes insignificant modifications to the conventional CSA circuit.
Latency overhead is just one cycle caused by the write back inclusion
Chart: 
Chart: 
| TC-Adder | LUPIS
Area overhead (%) | 200 | 21
[7]
[7]
Overhead
Notes: Text
Yeseong