## Slide 1
ASAP: A Speculative Approach to Persistence
Sujay Yadalam, Nisarg Shah, Xiangyao Yu, Mike Swift
{sujayyadalam, nisargs, yxy, swift}@cs.wisc.edu
University of Wisconsin-Madison

## Slide 2
Executive summary
Recoverable applications that use Persistent Memory (PM) require ordering of writes to memory
Commercially available systems are inefficient
State-of-the-art designs don't scale well in a multi-memory controller system with large number of cross-thread dependencies
  Flushing stalled for 1 in 4 cycles on average
ASAP uses eager flushing and speculative updates to efficiently order writes
Achieves performance close (within ~4%) to an ideal system

## Slide 3
Outline
Overview
Motivation
Existing designs
ASAP design principles
Results

## Slide 4
Persistent memory
Byte-addressable
High density
Non-volatile
Hardware encryption
Close to DRAM performance
Load/store interface
Intel Optane Persistent memory
Persistent memory (PM) enables recoverable applications with in-memory data structures
Notes: Preserve application progress across reboots and failures.

## Slide 5
Memory controller
Cache
Writeback
Core
Recovery requirements
Recoverability imposes order on writes to PM
Problem: cache hierarchy could re-order writes
*food
fish
Crash
Pointing to incorrect data
For correct recovery, data should be persisted before the pointer
fish
*food
onion
Notes: Recoverability requires a consistent state;
Application developers and hardware need to work together to ensure correct ordering

## Slide 6
Flush and Fence
Current systems use flush and fence for ordering
Intel x86 systems: CLWB and SFENCE
…
MOV a, 0x1234
MOV fish, 0xABCD
CLWB fish
SFENCE
MOV *food, Addr(fish)
Objective: Persist Data before Pointer
Epoch: group of unordered writes;
epochs ordered using fence.
E1:
E2:
E1 needs to be persisted before E2
fish
*food
a
fish
*food
FENCE
1
a
2
Timeline
Enforcing order causes stalls. Degrades performance.

## Slide 7
Memory controller
Cache
Core
Buffered Persistency
HOPS1 (ASPLOS ‘17), DPO2 (MICRO ‘16)
Buffer writes in a hardware queue, track ordering
Write them out lazily in-order
Persist Buffer
fish
Persist path
Decouples persistence from core execution
Ordering without stalling frequently
[1] S. Nalli et.al., “An analysis of persistent memory use with whisper,” in ASPLOS 2017.
[2] A. Kolli et.al., “Delegated persist ordering,” in MICRO 2016

## Slide 8
1) Ordering across memory controllers
Correct recovery requires ordering across controllers
Existing solutions use conservative flushing
  Writes to MC2 not flushed till writes to MC1 completes
Memory controller 1
Cache
Memory controller 2
Core
Conservative flushing leads to under-utilization of available system write bandwidth
fish
*food
ACK
fish
*food
Order:
(does not flush till ACK from MC1)
Notes: Cannot overlap writes to multiple memory controllers if separated by fence

## Slide 9
2) Cross-thread ordering
Cross-thread dependencies could arise
  Access to same address by 2 or more threads
  Synchronization between threads
Like before, existing solutions use conservative flushing
  Dependent thread stalls flushing till source thread completes its writes
A
B
Order:
Memory controller
Cache
Core 1
Core 2
Cache
PB
PB
A
B
Does not flush till core 1 finishes
Conservative flushing causes flushing stalls
C
D
E
Frequent flushing stalls fill up the buffers, exert back pressure on the cores by stalling them
Notes: Reduce time here;

## Slide 10
Cross-thread ordering
Cross-thread dependencies could arise
  Access to same address by 2 or more threads
  Synchronization between threads
Like before, existing solutions use conservative flushing
  Dependent thread stalls flushing till source thread completes its writes
Cross-thread dependencies are frequent
Conservative flushing causes flushing stalls
Frequent flushing stalls fill up the buffers, exert back pressure on the cores by stalling them
Notes: Explain figure in more detail;

## Slide 11
ASAP overview
Goals: 1) Utilize system write bandwidth efficiently
2) Avoid flushing stalls
Crashes are rare, so ASAP takes an optimistic approach:
  Flush writes eagerly and possibly out-of-order
  Speculatively update memory with “early” writes
  Maintain recovery information to revert changes in case of crashes
Key insight: Intel ADR* feature allows some data in memory controller queues to be persisted after power failure; can use ADR to store fix-up information
* ADR = Asynchronous DRAM refresh
Notes: Say ADR is a feature in today’s systems

## Slide 12
Eager flushing
E0,1
E0,2
E0,0
T0
E1,1
E1,2
E1,0
T1
Ordering
Currently flushing
Waiting
Completed
Conservative Flushing
E0,0
E1,0
E0,1
E1,1
E0,1
E0,2
E0,0
T0
E1,1
E1,2
E1,0
T1
Eager Flushing
E0,1
E1,1
E1,2
E0,2
Persist buffers in ASAP flush writes as soon as they arrive
Doesn’t stall waiting for previous epochs to complete
Flushes are marked ‘safe’ or ‘early’
Core
Cache
Persist
Buffer
Notes: Color consistency;
Maybe leave out ET here

## Slide 13
Tagging ‘early’ flushes
Epoch Tables (ET) stores epoch metadata
Tracks ordering dependencies between epochs
  Including dependencies across threads
ET determines if a flush is ‘safe’ or ‘early’
  safe if previous epochs complete
  early if previous epochs are still flushing
TS
Pending Ack
Src TS
32b
5b
8b
Epoch Table
Dependent
ThreadID
32b
8b
MC
bit vec
16b
Src
ThreadID
Core
L$
Persist
Buffer
ET
Notes: Figure in the same place;
Relation between safe and conservative flushing

## Slide 14
MC
Handling early flushes
Memory controllers in ASAP also take an optimistic approach
On receiving ‘early’ flush, tries to update memory speculatively
Read old value from memory before updating
Create undo record using the old value
Store these records in recovery table (RT) backed by ADR
Shared LLC
DRAM
PM
Recovery Table
B
(early)
B

## Slide 15
Freeing space in RT
ET sends commit message to memory controllers after
  After all flushes in an epoch complete AND
  Dependencies are resolved
Memory controllers delete undo records belonging to that epoch
ET
Memory controller
Cache
Core 1
Core 2
PB
PB
ET
Epoch
commit
Cache
RT

## Slide 16
ET
ASAP in action
Memory controller
Cache
Core 1
Core 2
Cache
PB
PB
A
B
Order:
A
Undo record:
B = old value
commit
ACK
Epoch complete
Read value of B
(early)
RT
B

## Slide 17
A=0
Write collisions
Undo logs are insufficient when multiple threads write to same address
Memory controller
Cache
Core 1
PB
Cache
Core 2
PB
Cache
Core 3
PB
A=1
A=2
A=1
A=2
Order:
A=3
ASAP handles such collisions by creating delay records
Delay records are stored in the recovery tables
They are written out later (or discarded) when epoch commit is received
Undo A=0
Redo A=2
ET
ET
ET
A=3

## Slide 18
Outline
Overview
Motivation
Existing designs
ASAP design principles
Results

## Slide 19
Evaluation setup
gem5 full system simulations
System config:
  4 CPU cores based on Intel Xeon processors
  2 memory controllers
  PM characteristics modelled using real world experiments
[1] S. Nalli et.al., “An analysis of persistent memory use with whisper,” in ASPLOS 2017.
Workloads:
  WHISPER1 benchmark suite
  Custom data-structures using ATLAS framework
  Data structures designed for PM (CCEH, RECIPE)
Notes: We aimed to study the performance benefits of eager flushing. We ran experiments to understand how well ASAP performs compared to existing solutions that use conservative flushing. We were also interested in determining how close ASAP was to an ideal system.

## Slide 20
Performance comparison
Notes: Explain what is baseline; no PBs, go through caches;
Speedup “normalized”

## Slide 21
Performance comparison

## Slide 22
Performance comparison
Large number of cross-thread dependencies
ASAP improves performance by ~23% on average

## Slide 23
Performance comparison
ASAP performance close to ideal (within ~4%)
Notes: What is an ideal system? No overhead of ordering and persistence, flushing cost, immediate persistence

## Slide 24
Bandwidth utilization
Micro-benchmark: Alternating writes to 2 memory controllers separated by a fence
ASAP improves bandwidth utilization by 2x
while i < n:
MC1 = rand_val();
FENCE
MC2 = rand_val();
HOPS unable to flush writes to both memory controllers simultaneously
Notes: For more results such as how ASAP scales with more cores; and effect of eager flushing on buffer occupancies and write amplification, please read our paper.

## Slide 25
Conclusion
Recoverable applications using PM require correct ordering of writes
State-of-the-art designs are not efficient at
  Ordering across memory controllers
  Ordering across threads
ASAP uses an optimistic approach:
  Flushes writes eagerly
  Updates memory speculatively while maintaining some fix-up info in case of crashes
ASAP improves performance over existing solutions by ~23% and within 4% of an ideal system

## Slide 26
ASAP: A Speculative Approach to Persistence
Sujay Yadalam, Nisarg Shah, Xiangyao Yu, Mike Swift
University of Wisconsin-Madison
sujayyadalam@cs.wisc.edu
https://github.com/multifacet/ASAP

## Slide 27
Crash recovery
During a crash, ADR lets undo records in the recovery tables (RT) to be written out to memory
Memory controller
Cache
Core 1
Core 2
Cache
PB
A
B
Order:
A
B
B’s old value
PB
RT
Crash
Consistent state
ET
ET

## Slide 28
MC
MC
ASAP system overview
Core
Cache
Epoch Table
Persist
Buffer
Shared LLC
Core
Core
Core
DRAM
PM
DRAM
PM
Recovery Table
2
1
1
2
3
Persist path
Epoch commit
Epoch completion
PB
PB
PB
ET
ET
ET
3
Cache
Cache
Cache

## Slide 29
Flush and Fence
Current systems use flush and fence for ordering
Intel x86 systems: CLWB and SFENCE
MOV Data, 0x007
CLWB Data
SFENCE
MOV Pointer, Addr(Data)
Enforcing order causes stalls. Degrades performance.
Objective: Persist Data before Pointer
data
*p
FENCE
1
2

## Slide 30
ASAP overview
Goals: 1) Utilize system write bandwidth efficiently
2) Avoid flushing stalls
Crashes are rare, so ASAP takes an optimistic approach:
  Flush writes eagerly and possibly out-of-order
  Speculatively update memory with “early” writes
  Maintain recovery information to revert changes in case of crashes
Key insight: Intel ADR allows some data in memory controller queues to be persisted after power failure; can use ADR to store fix-up information

## Slide 31
Eager flushing
Avoids flushing stalls and
Utilizes system write bandwidth efficiently
Conservative flushing
Eager flushing

## Slide 32
Persist buffers
Per-core volatile circular buffers
Writes to PM enqueued in PBs
Writes tagged with timestamp (TS) to track order
Writes flushed eagerly
Flushes labelled ‘safe’ or ‘early’
  Epoch Tables helps in labelling

## Slide 33
Epoch tables
Per-core volatile buffers
Stores metadata of in-flight epochs
Uses coherence to detect cross-thread dependencies
Notifies other cores and memory controllers of epoch completions

## Slide 34
Performance study

## Slide 35
Recovery Tables
Buffers in the memory controllers
Belong to persistent domain, backed by ADR
Stores recovery information: undo records and delay records
On receiving an ‘early’ flush, memory controller
  Reads old value from memory to create undo record
  Updates memory specualtively